## Slide 1
https://github.com/Sphaeralcea/TTL_Calculator_4_Banger
Video Clip

## Slide 2: TTL 4-Banger Calculator
Features and Requirements
All 74hcXX logic implementation (plus 3 4XXX) chips, 77 total, and one 2816 EEPROM
Purpose built architecture (not a CPU architecture)
RPN style operation (HP Enter key)
Add, subtract, multiply, and divide, clear entry, clear all
8 numeric digits plus an Error and sign digit
  Max num: +99,999,999 to -99,999,999
  Min Num: +0.0000001 to -0.0000001
Floating decimal point
Signals error on overflow for all operations, keyboard input overflow, and divide by 0
Underflow handling
Leading zero blanking during operand entry
Running total operation (last result = Operand1 + Enter)
All rising edge flip-flop design
All on a single PCB
3 Major logic blocks
SEQ: Micro-sequencer engine with 2Kx8b uROM
  24-bit micro-instruction word
  Unconditional branch, 16 conditional branches, 1 NMI-type interrupt
  Single level loop counter (no nesting)
  Clock and reset generation
DSKY: Keyboard and Display unit
  9-digit LED display sequencing,
  18(20)-key keyboard encoding (2 keys not used)
REG: Register-Arithmetic unit
  3, 8-digit registers (4-bits X 8)
  1 digit BCD adder/subtractor and exponent calculator (counters)
  8 status and control register bits, operation progress tracking state machine
Architectural deficits (intentional)
  No rounding logic
  No guard digits
Architectural bugs (unintentional)
  Accuracy loss dividing 2 8-digit integers
  Underflow condition in addition not accounted for
  No trailing zero blanking

## Slide 3: Top Level Process View
1 | 2 | 3 | + | Clr
4 | 5 | 6 | - | CE
7 | 8 | 9 | X | 
0 | , | Ent | / | 
Txt File
Arduino Sketch
Arduino Nano
2816
2816 Programmer
DSKY
Xreg
Yreg
Qreg
X9
QL
Add/Sub
MetaData
Status
Trk SM
Rst
REG
uROM
Pwr-On
Rst Clocks
Bra
Int
SEQ
TTL 4-Banger PCB
uInstr
Branch Conditions
Int
Spreadsheet
MicroCode
2816
ROM
image
Sim
ROM
image
Logisim Evolution
RTL Simulation Schematic
Sim
ROM
Model
Manual Schematic Translation
Manual Functional Verification
Design
Entry
Schematic Entry
uCode Entry
EasyEDA/JLCPCB
Schematic
PCB
(Autoroute Modules
+
Manual Connect Modules)
LTSpice
Clk
Rst
Disp
Analog Parts
BreadBoard
Design Feedback

## Slide 4
Seq
Counter
Ph4
Gate
Cond
Bra
Mux
15 HW
Indications
Bra
Logic
HW Interrupt
IntrptVector[6:2]
ImmData[3:0]
uInstrBits[5:23]
Clk
Rst
Phs
Cntr
Phs
Dec
Ph1
Ph2
Ph3
ph4
uROM
2Kx8
ClkX, ClkY
SEQ
Microsequencer
E
Loop
Cntr
ClkX
ClkY
Ph1B
D0
D1
D2
D3
I5Bra
I6
I7
I8
I9
I10
I11
I12
I13
I14
I15
I16
I17
I18
I19
I20
I21
I22KeyAckB
I23HWIntEn
0-14
15
CSelCtl1
CSelCtl2
CSelCtl2
SubAddB
CarryEn
XCmd
YCmd
QCmd
Clk1
E
E
p1
p2
p3
8
8
8
8
11
19
Jmp(I4)
Bra(I5)
LoadAddr
BraAddrSel
4
Loop Cnt Exp
I4Jmp
E#
E
11
BraAddr I[18:8]
HWIntEn(I23)
BraSel[3:0]
Assembles 24-bit uInstruction from 3 consecutive reads of uROM.
3 Instruction Types:
uINSTR
JMP <target>
BRA <cond_sel> <target>
Target
Addr

## Slide 5
Power-On Reset Startup
p1
p2
P3
P4
p1
p2
P3
P4
p1
p2
P3
P4
p1
p2
P3
P4
PhaseCnt
Ph1
Ph2
Ph3
Ph4
0
1
2
uROMaddr
3
4
5
6
7
8
9
A
B
0V
Vcc
Rst
RstB
Clk1
Vi
Vcc
~2V
In reset
Operational
Pwr On
Vcc
Gnd
Rst
RstB
12K
10uF
Clk1
Gnd
0.0022uF
5.6K
Vi
t

## Slide 6: Sequencer (SEQ)
Includes Clock, Reset and Timing generation.
  Schmitt trigger reset holds sequencer in reset until power rises to ~75% VCC.
  Schmitt trigger oscillator generates 1X clock.
  1X clock drives SEQ logic only. Does not clock other units.
  1X clock feeds the uInst PC, the IR, and the phase counter which also generates the div4 clocks, ClkX and ClkY.
  ClkX and Clky clock other units.
Sequencer operates on a 4-phase instruction cycle to construct and present a 23-bit micro-instruction to hardware.
  First 3 phases read three consecutive bytes from uROM and stores them in 3 8-bit registers.
  During first 3 phases, external hardware sees 0’s (inactive) on all signals.
  Fourth phase ungates the uInstruction and presents it to external hardware.
  D0 – D3: Immediate data and select field
  I4: Flow control field. This bit is reserved for the sequencer’s exclusive use
    I4=0: Entire instruction is uINSTR type
    I4=1: Instruction is flow control (JMP or BRA)

## Slide 7: Sequencer (SEQ)
I5: HW control and flow control qualifier.
  If I4=0, then I5 is just another iINSTR bit
  If I4=1, then I5 is flow control qualifier.
    I5=0, unconditional
    I5=1, conditional
      One of 16 conditions may be tested, selected by D[3:0]. If condition is true then branch is taken.
      D[3:0]=0xF is reserved. Dedicated internally to implement a simple for-loop capability.
I6 – I21: uINSTR bits
I22: Loop Init: Used internal to SEQ to reset a counter that implements a simple for-loop capability.
  I22 is also used as a uINSTR bit keeping in mind its SEQ internal use
I23: Interrupt enable. Used internal to SEQ to enable a hardware-initiated jump to be taken if external hardware has asserted the HWInt signal when I23 asserts
  External hardware provides the target address through a 6-bit vector, IV[6:2]
  The target address is formed by appending IV[6:2] with b00
    Hardware jump targets are confined to uROM addresses at 4-byte boundaries between 0x10 to 0x7C
  I23 may also be used as a uINSTR bit keeping in mind its SEQ internal use

## Slide 8: Sequencer (SEQ)
A primitive looping structure provides the ability to create loops up to 9 iterations (0-8)
  Loop counter reset by asserting I22 (InitLP8)
  Loop count tested and incremented by a conditional jump with D[3:0]=0xF (BRLoop8NZ)
  Loop count expires when loop count reaches 8 and loop will fall through on the next loop count test (BRLoop8NZ)
Note: There is no subroutine call and return capability provided.
  Since all keyboard service routines return to the keyboard-display loop, an unconditional JMP to this loop serves as an adequate return from keyboard service routines.

## Slide 9
p1 p2 p3 p4
p1 p2 p3 p4
p1 p2 p3 p4
p1 p2 p3 p4
p1 p2 p3
p1 p2 p3 p4
A1
A2
A3
D1
D1:D2
D1:D2:D3
D[0:3]
I[19:23]
I[5:18]
uROMaddr
uInst[0:7]
uInst[8:15]
uInst[16:23]
uInst[0:23]
Clt3[0:2], KeyAck,
HWIntEn
D[0:3]
Ctl1[0:2],Xcmd[0:1],Ycmd[0:1],
Qcmd[0:1], SubAddB, CarryEn, Ctl2[0:2],
D1
D2
D3
ClkX,Y
Clk1
Sequencer Instruction Timing
I4 (Jmp, Bra)
I8:18=An
An
An+1
An+2
I23
(HWIntEn)
IV[2:6]
IntAddr
IntAddr[0:7]=(00< IV >0)
IntAddr+1
IntAddr+2
I22
(IntAck)
Interrupt
Jump or Branch
Instruction Cycle
I5=[0,1], I6=I7=0

## Slide 10
0
1
2
3
8 7 6 5 4 3 2 1 0
Sel[8:0]
1:10
Dec
Pri
Enc
1 2 3 4 5
5
3
ImmData[3:0]
ImmData[1,2]
IV[6:2], HWInt
7 Seg
SDec
XDig0[3:0]
SignSeg
ErrorSeg
Xdp[2:0]
1:8
Dec
KeyAck
DSKY
Display and Keyboard
uSEQ
REG
KeyDet
Col
Row
Key
Reg
En
REG
1 2 3 + Clr
4 5 6 -- x1
5 6 7 X x2
0 . Ent / x3
Row
Col
Dp
7
DigE Dig7 Dig6 Dig5 Dig4 Dig3 Dig2 Dig1 Dig0
Segs
DigSel
8
CA
Scan Sequence
9 – Display enabled
0 – Dig0
1 – Dig1
2 – Dig2
3 – Dig3
4 – Dig4
5 – Dig5
6 – Dig6
7 – Dig7
8 – Dig8; Display disabled
0 – KeyRow1
2 – KeyRow2
4 – KeyRow3
6 – KeyRow4
Sel[0,2,4,6]
Sel9
Sel8
BIanking
KeyBrd
Disp
Ctl
disable
enable

## Slide 11: Display and Keyboard (DSKY)
DSKY is a passive module with no autonomy. Completely controlled by SEQ
Display and keyboard scan is performed via D[3:0] from SEQ
  The display is enabled by D[3:0]=b1001, and it is disabled by b1000
  Dig0 is activated by D[3:0]=b0000, Dig7 by b0111, the Sign/Error digit by b1000
  Row 0 of the keyboard matrix is activated by b0000, row 1 by b0010, row 2 by 0100, and row 3 by b0110. If the display is enabled, digit 0, 2, 4, and 6, respectively, are activated with the keyboard row
REG provides BCD data for each digit to display, 3-bit decimal point position, and the sign and error segments
When a key is pressed in an activated row, a key detect signal is raised
If microcode running on SEQ tests the detect signal to be true, then it may assert the KeyAck (I22) signal back to DSKY which registers the row and column where the depressed key resides and asserts the HWInt signal
On any microcode instruction that asserts HWIntEn (I23) while HWInt is asserted, SEQ flow will jump to the microROM address formed by the concatenation of col[2:0], row[1:0], and b’00.

## Slide 12
D[3:0]
CircX
ClkX
Display Output
D[3:0]
RowHold
Asserted Row
KeyDet
Column Activated
IV[6:2]
KeyAck
DispEnable
HWIntEn
DSKY LOOP
0
1
2
3
4
5
6
7
8
9
0
2
4
6
2
4
6
0
X
X
XDig0
Xdig2
Xdig3
Xdig5
Xdig6
Xdig7
Xdig1
Xdig4
E/Sig
0
2
X
X
4
X
X
X
X
X
6
X
X
3
(01111b)
XX
Tst KeyDet
Bra KeyRel
Tst KeyDet
Bra KeyRel
Key Release Loop
0
9
IV[7:0]=00111100=3Ch=“Enter” key
Top of DSKY Loop
Top of DSKY Loop
DSKY Loop Branches away to
Interrupt Service Routine
Display Sequence
Keyboard Scan
Sequence
Release Loop Exit
HWInt
HW
Interrupt
Display Scan
Sequence
“Ent” Key Pressed
“Ent” Key Released
X
X

## Slide 13
0
0
QL
X9
0
XREG
YREG
QREG
LSDout
MSDout
LSDout
LSDout
MSDout
LSDin
MSDin
LSDin
MSDin
MSDin
MSDout
LSDin
Cmd
Cmd
Cmd
HOLD,SHL,SHR
HOLD,SHL,SHR
HOLD,SHL,SHR
ARITH
Oprnd1
Oprnd2
Sum
Cmd
ADD,SUB,CARRYEN
IMMDATA
msd
lsd
SHR
SHL
X,Y,QREG
DSKY
SEL[Dat,Q]
SEL[0,X]
SEL[X9,SUM,X,Y]
SEL[0,Y,X]
SEL[0,QL]
uSEQ Microinstruction Bits
SubOp Tracking &
Status Bits
REG
Register and Math
SETBITS, NXTPH
XDig0]3:0]
NC
NC
ENABLE, LOAD, CNTUP/DN
ENABLE, LOAD, CNTUP/DN
.
.
.
SEQ
0
0
0
Xreg
Yreg
Qreg
+
-
Key
Basic Traffic
STATPHSRST

## Slide 14: REG: Registers, Data Steering and Compute
REG is a passive unit with no autonomy. Completely controlled by SEQ
Three Registers; XReg, YReg and QReg are each arrays of 8 BCD (4-bit) digits
  Each register supports shift operations; either SHR, SHL, or both. SHR moves digits one position from MSD (most significant digit) to LSD, and the current LSD exiting the register with SRC replacing the MSD. SHL moves digits from LSD to MSD and the MSD exiting the register with SRC replacing the LSD.
    SHRX SRC: X9, SUM, XLSD, YLSD
    SHLX SRC: IMMData, QMSD
    SHRY SRC: Zero, YLSD, XLSD
    SHRQ SRC: Zero, YLSD
    SHLQ SRC: Zero, QLSD
  Each register may operate individually or in tandem with others but only limited cases of simultaneous register shifting are supported. Examples include: Exchange the values of Xreg and Yreg; Adding Xreg and Yreg, with SUM replacing Xreg while Yreg circulates (or is replaced with zero); Copy Xreg to Yreg while Xreg circulates (or is replaced with zero)
X9 and QL are single BCD digit registers (loadable counters), auxiliary to Xreg and reg, respectively.
  X9 accumulates carries out of Xmsd for Addition and Multiplication operations and is used to test Xreg digits for 0.
  QL is used for Multiplication as a loop counter and for Division as partial quotient accumulator
  Each can increment or decrement by one and each is loadable from two sources:
    X9 SRC: Zero, XMSD
    QL SRC: Zero, QLSD

## Slide 15: Arith – Add/Sub
Arith is a single digit BCD adder/subtractor that operates only on XLSD and YLSD. The output of Arith is the SUM routed only to XMSD
  Additional outputs indicate if the add generated a carry out and if the result of a subtraction is a negative number.
  Subtraction is done through 10s complement arithmetic.
The Add/Sub block is implemented with a cascade of three combinational logic stages:
  10’s complement of one input
  Summing the inputs
  BCD correction of result
The CarryO bit is valid for exactly one clock following the sum. This imposes a requirement for any operation on multi-digit numbers be carried out with contiguous add instructions (no intervening cycles)
The IsNeg bit is valid for exactly one clock following the sum. This requires that action to be taken as a result of the IsNeg signal is immediate.
If the result of a subtraction is negative, the 10’s complement result is stored in Xreg and additional uCode performs subtraction of the result from 0, returning the desired result
Arith includes 4 counters that react to key strokes to compute sum of exponents, difference of exponents, digit count, and decimal point position

## Slide 16: Arith – Metadata Counters
Arith includes 4 counters that react to key strokes to compute sum of exponents, difference of exponents, digit count, and decimal point position
  Incremented or decremented by microcode instructions
    XDigCnt – increments for each numeric key. If zero(s) is the first keystroke, it is not counted
    XDpCnt – increments for each numeric key after the decimal point (counts digits in fractional portion of operand)
    SexpCnt, DexpCnt – hold the sum and difference, respectively, of the exponents of the two operands
      Positive Exponent - first key of operand is numeric. Increment for each numeric key until decimal point is keyed
      Negative Exponent - first key of operand is decimal point key. Decrement for each leading zero keyed until non zero numeric key
      SexpCnt
        for each operand, positive exponents increment up, negative exponents decrement down
      DexpCnt
        for first operand, positive exponents increment up, negative exponents decrement down
        For second operand, negative exponents increment up, positive exponents decrement down
Via microcode instructions, DexpCnt can be transferred to SexpCnt. SexpCnt can be transferred to XDpCnt. DexpCnt can be transferred to XDpCnt in two steps

## Slide 17: StatPhsRst
There are two reset domains for sequential logic in REG, X and Y.
  The Xreg domain includes Xreg and state associated with Xreg.
    X reset is triggered by a microcode instruction and by the transition from entering the first operand to entering the second operand
  The Yreg domain includes Yreg and Qreg and associated state.
    Y reset is triggered by a microcode instruction
  The Rst part of StatPhsRst is a reset synchronizer to filter spurious logic glitches from SEQ on X and Y domain resets
The Stat part of StatPhsRst is an array of status bits to store sign bits for operands and exponents and other state information needed to parse keystrokes. Bits are set and cleared by microcode instructions and by reset events

## Slide 18: StatPhsRst
The Phs part of StatPhsRst is a state machine that tracks the phase of the operation underway. Its state variables are tested by branch instructions
States include
  Idle* – System has cycle through reset but no keys have been pressed (virtual state)
  Op1Ph* – First operand is being entered (virtual state)
  EOp1Ph – First operand is entered but second operand has not started
  Op2Ph – Second operand is being entered
  OprPh – One of the 4 operations is underway
  MultDivPh – One of either the mult or div operation is underway
  * Idle state and Op1Ph state do not need actual state variables but they represent operational
  states of the overall machine
The state machine is advanced by a microcode instruction
  The transition from EndOp1 to Op2Ph will also happen with the first key starting operand2

## Slide 19
XDigCnt
XDpCnt
DexpCnt
SExpCnt
NegExpFixed
Error
SignYexp
SignXexp
SignY
DpFree
SignX
Status Bits
Op Phase
Tracking
State Machine
Yreg
Xreg
Sub
CarryEn
Sum
CarryO
IsNeg
4
4
4
CntUp/Dn
XDigSel
XDpSel
DexpSel
SexpSel
XdigEq0
XDigFull
XDpOvrfl
XDp
3
DexpOvrfl
4
4
Sexp
Dexp
DexpEq0
MetaData Counters
BCD Add/Sub
StatBitEn
StatBitVal
Reset Sync
ClrXA
ClrYA
ClrX
ClrXB
ClrY
ClrYB
NxtPh
KeyEnt
MultDivPh
OprPh
EoPh1
Op2Ph
Arith
EOP1PH
OP2PH
OPRPH
MULTDIVPH
“Ent” (NxtPh)
“0-9, -, .” (KeyEnt)
“+, -” (NxtPh)
“*, /” (NxtPh, NxtPh)
“0-9, .” (KeyEnt)
“0-9, .” (KeyEnt)
“Clr”
Any State
“0-9, -, .” (KeyEnt)
Virtual States
IDLE
(DSKY)
OP1PH
OPRPH
Always
Op Phase Tracking SM
10’s Compl
BCD
Fix
Rst
Phase SM
StatPhsRst
StatBitSel[2:0]
+
Ci

## Slide 20
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
0
1
2
3
Op1+Op2+Ci
Co Sum1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
C SUM
9
SUM
CarryO
+
Ci
Co
+
Ci
Co
Op1
Op2
Ci
BCD Correction
>
0
6
1
Sum1(R16)
Sum2(R10)
BCD Addition
A+B; A, B in {0..9] BCD
Sum in [0..15]Hex -> [0..18]BCD
7
+ 5
-----
0xC If Sum>9 Then
+ 6 Add 6 to Sum
-----
12 bcd
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
Decimal addition translated
to base 16 wheel:
7
+5
Carry a 1
12
9
+ 8
------
0x11 If Hex Rollover
+ 6 Add 6 to Sum
------
17 bcd
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
Decimal addition translated
to base 16 wheel:
9
+8
Carry a 1
17

## Slide 21
For an n digit decimal number DnDn-1…D1D0;
The 10s complement is the 9s complement plus 1;
Which is:
{9-Di; for each Di (i in 0 to n)} + 1
This is the same as:
{(0xF-Di+10)mod16; for each Di (i in 0 to n)} + 1
This is the same as:
{(1’sComp(D)+10)mod16; ; for each Di (i in 0 to n)} + 1
9 9 9
-2 -9 -0
7 0 9
+ 1
7 1 0
9s comp
10s comp
F
-2
D
+A
7
F
-9
6
+A
0
+
F
-0
F
+A
9
1
Mod 16
Mod 16
Mod 16
710
0
1
2
3
4
5
6
7
8
9
9
-2
9s Complement: 9-2
10’s Complement
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
F-9+10 = 1sComp(9) + 10
9-2 = (F-2+10)mod16 = [1sComp(2)+A]mod16
10’s complement of 290
7
0
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
F
-0
+10
F-0+10 = 1sComp(0) + 10
9
709
+ 1
------
710 = 10’s complement of 290
F
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
F
-2
+10
+10
-9
0
1
2
3
4
5
6
7
8
9
9
-2
10s Complement: (9-2)+1
+1
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
F
-2
+10
10s Complement translated
to base 16 wheel: (F-2)+10+1
+1
0
1
2
3
4
5
6
7
8
9
9s complements
9s Complement

## Slide 22
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
0
1
2
3
-9
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
9
SUM
Co A + 10#(B)
Op1-Op2
-9
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
9
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
+
Ci
Co
+
Ci
Co
Op1
Op2
A
1
9
CarryO
+
Ci
Co
BCD Correction
>
0
6
1
1s comp
+
Ci
Co
A
1s comp
1
SUM
IsNeg
10’s Comp
10’s Comp
Sum1(R16)
Sum2(R10)
BCD Subtraction

## Slide 23
Reset Vector (CLR)
Interrupt Vector Table
DSKY Loop
Interrupt Routines
  ZERO
  ONE
  TWO
  THREE
  FOUR
  FOVE
  SIX
  SEVEN
  EIGHT
  NINE
  DP
  CLR
  CE
  ENTOP1
  MINUS
  SUB
  PLUS
  MULT
  DIV
HWIntEn
Display Enable
Display XDig0
Display XDig1
Display XDig2
Display XDig3
Display XDig4
Display XDig5
Display XDig6
Display XDig7
Display DigError
Display Disable
Activate Row0, Sense Columns
Activate Row1, Sense Columns
Activate Row2, Sense Columns
Activate Row3, Sense Columns
JMP ONE
JMP FOUR
JMP SEVEN
JMP ZERO
JMP TWO
JMP FIVE
JMP EIGHT
JMP DP
JMP THREE
JMP SIX
JMP NINE
JMP ENTOP1
JMP PLUS
JMP MINUS
JMP MULT
JMP DIV
JMP CLR
JMP CE
JMP X2(CLR)
JMP X3(CLR)
MicroCode Organization
0x006
0x010
0x060
0x11D
0x22B
0x57C

## Slide 24
MicroCode Sample

## Slide 25
MicroCode Fields, Mnemonics and Codes
 | Jmp/Bra | 1[4] | 1[3:0] |  | RegCmd | 2[5:0] |  | SelCtl1 | 1[7:5] |  | SelCtl2 | 3[2:0] |  | CtlSel3 | 3[5:3] |  | KeyMCntSel | 1[3:0]
 | JMP | 1 | 0000 |  | CircX | 000001 |  | SelXReg | 001 |  | ClrXPh1 | 001 |  | SelQLQlsd | 001 |  | 0 | 0000
BR0 | BRDecEven | 1 | 0000 |  | DPAdjX | 000001 |  | LoadX9 | 010 |  | ClrYPh2 | 010 |  | SelYQYlsd | 010 |  | 1 | 0001
BR1 | BRDigFull | 1 | 0001 |  | EntNumX | 000010 |  | SelXQmsd | 011 |  | StatBitEn | 011 |  | StatBit1 | 011 |  | 2 | 0010
BR2 | BRDigEmpty | 1 | 0010 |  | LeftJustX | 000010 |  | LoadQL | 100 |  | SelXYlsd | 100 |  | SelX9Xmsd | 100 |  | 3 | 0011
BR3 | BRDintOvrfl | 1 | 0011 |  | DPAdjY | 000100 |  | SHDexpXDP | 101 |  | SelXSum | 100 |  | SelYXlsd | 101 |  | 4 | 0100
BR4 | BRSignX | 1 | 0100 |  | CopyXY | 000101 |  | Reserved1 | 110 |  | NxtPh | 101 |  | CntrIncr | 110 |  | 5 | 0101
BR5 | BRSignY | 1 | 0101 |  | ExchXY | 000101 |  | Reserved2 | 111 |  | CntrEn | 110 |  | RowHold | 111 |  | 6 | 0110
BR6 | BRInOp2Ph | 1 | 0110 |  | AddSub | 000101 |  | HWINTEN | 000 |  | SHSexpDexp | 111 |  | SelYZero | 000 |  | 7 | 0111
BR7 | BRDPFree | 1 | 0111 |  | DivXY10 | 000101 |  | SelXData | 000 |  | SelXX9 | 000 |  | SelQZero | 000 |  | 8 | 1000
BR8 | BRQLZero | 1 | 1000 |  | ShrX9X8QDiv10 | 010001 |  | SelXSumX9 | 000 |  | SelXXlsd | 000 |  | SelX9Zero | 000 |  | 9 | 1001
BR9 | BRX9Zero | 1 | 1001 |  | CopyYQ | 010100 |  | ExtraSelCtl1 | 000 |  | ExtraSelCtl1 | 000 |  | SelQLZero | 000 |  | BlankNum | 1111
BR10 | BRDpOvrfl | 1 | 1010 |  | CopyQX | 100010 |  | ExtraSelCtl2 | 000 |  | ExtraSelCtl2 | 000 |  | ExtraSelCtl3 | 000 |  | XDigCnt | 0001
BR11 | BRNoKeyDet | 1 | 1011 |  | ApendDivdn | 000010 |  | ExtraSelCtl3 | 000 |  |  |  |  |  |  |  | XDPCnt | 0010
BR12 | BRIsNeg | 1 | 1100 |  | RmLdZeroX | 000010 |  | ExtraSelCtl4 | 000 |  | ALUCmd | 2[7:6] |  | SEQ/DSKY | 3[7:6] |  | XYDexpCnt | 0011
BR13 | BRCarryO | 1 | 1101 |  | CopyQ0QL | 100000 |  |  |  |  | SubXY | x1 |  | HWINTEN | 10 |  | XYSexpCnt | 0100
BR14 | BRSignXexp | 1 | 1110 |  | ShrX | 000001 |  | BR* | 001 |  | CarryEn | 1x |  | KeyAck | 01 |  | X9Cnt | 0101
BR15 | BRLoop8NZ | 1 | 1111 |  | ShlX | 000010 |  |  |  |  |  |  |  | InitLP8 | 01 |  | QLCnt | 0110
 | BRSignYexp | 1 | 0110 |  | CopyYX | 000101 |  |  |  |  |  |  |  |  |  |  | FixDP | 0000
 | BrNegExpTerm | 1 | 0101 |  | ExtraCmd3 | 000000 |  |  |  |  |  |  |  |  |  |  | SignXexp | 0001
 | ExtraBR2 | 0 | 0000 |  |  |  |  | ImmData asserts on Ph2 of each cycle |  |  |  |  |  |  |  |  | NegExpTerm | 0010
 | ExtraBR3 | 0 | 0000 |  |  |  |  | SelCtl1, SelCtl2, RegCmd, ALUCmd assert on Ph4 and is valid only Ph4 |  |  |  |  |  |  |  |  | SignX | 0011
 | HWINTEN | 0 | 0000 |  |  |  |  | SelCtl3, KeyAckB, HWIntEn Assert on Ph4 of each cycle |  |  |  |  |  |  |  |  | SignY | 0100
 |  |  |  |  |  |  |  | SelCtl3 Can assert simutaneous with JMP/BR*. SelCtl1/2 cannot. |  |  |  |  |  |  |  |  | SignYexp | 0101
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | AssertError | 0110

## Slide 26
SelXReg | 001 | Select X reg MSD source from X reg or Y reg group
LoadX9 | 010 | Load X9 source into X9 reg
SelXQmsd | 011 | Select X reg source from Q Dig7
LoadQL | 100 | Load QL source into QL reg
SHDexpXDP | 101 | Load Dexp counter value into XDP counter
Reserved1 | 110 | Currently unassigned
Reserved2 | 111 | Currently unassigned
SelXData | 000 | Select X LSD reg source from D[3:0]
SelXSumX9 | 000 | Select X reg MSD source from Sum or X9 group
ClrXPh1 | 001 | Clear X reg domain devices
ClrYPh2 | 010 | Clear Y reg domain devices
StatBitEn | 011 | Enable status latches for write
SelXYlsd | 100 | Select X reg MSD source from Y reg LSD
SelXSum | 100 | Select X reg MSD source from SUM
NxtPh | 101 | Advance tracking state machine state
CntrEn | 110 | Enable selected counter for up/down advance
SHSexpDexp | 111 | Load Sexp counter value into Dexp
SelXX9 | 000 | Select X reg MSD source from X9 reg
SelXXlsd | 000 | Select X reg MSD source from X reg LSD
SelQLQlsd | 001 | Select QL reg source from Q reg LSD
SelYQYlsd | 010 | Select Y and Q reg MSD sources from Y reg LSD
StatBit1 | 011 | Set selected status bit to 1
SelX9Xmsd | 100 | Select X9 reg source from X reg MSD
SelYXlsd | 101 | Select Y reg source from X reg LSD
CntrIncr | 110 | Increment selected and enabled counter
RowHold | 111 | DSKY row latch disable (hold)
SelYZero | 000 | Select Y reg MSD source from 0
SelQZero | 000 | Select Q reg MSD source from 0
SelX9Zero | 000 | Select X9 reg source from 0
SelQLZero | 000 | Select QL reg source from 0
CircX | 000001 | Shift X reg from MSD toward LSD
DPAdjX | 000001 | 
ShrX | 000001 | 
EntNumX | 000010 | Shift X reg from LSD toward MSD
LeftJustX | 000010 | 
ApendDivdn | 000010 | 
RmLdZeroX | 000010 | 
DPAdjY | 000100 | Shift X reg from MSD toward LSD
CopyXY | 000101 | Shift X and Y reg from MSD toward LSD
ExchXY | 000101 | 
AddSub | 000101 | 
DivXY10 | 000101 | 
ShrX9X8QDiv10 | 010001 | Shift X and Q reg from MSD toward LSD
CopyYQ | 010100 | Shift Y and Q reg from MSD toward LSD
CopyQ0QL | 100000 | Shift Q reg from LSD toward MSD
CopyQX | 100010 | Shift X and Q reg from LSD toward MSD
JMP | NA | Unconditional Branch
BRDecEven | 0000 | Branch if DexpCnt=0
BRDigFull | 0001 | Branch of DigCnt=8
BRDigEmpty | 0010 | Branch if DigCnt=0
BRDintOvrfl | 0011 | Branch if Dexp>=8
BRSignX | 0100 | Branch if SignX status bit set
BRSignY | 0101 | Branch if SignY status bit set
BRInOp2Ph | 0110 | Branch if in or beyond Op2Ph tracking state
BRDPFree | 0111 | Branch of DP status bit has not been set
BRQLZero | 1000 | Branch if Qlreg=0
BRX9Zero | 1001 | Branch if X9reg=0
BRDpOvrfl | 1010 | Branch if XDpCnt>=8
BRNoKeyDet | 1011 | Branch if no key is currently pressed
BRIsNeg | 1100 | Branch if arithmetic (SUM) sign bit is set
BRCarryO | 1101 | Branch if arithmetic carry out bit is set
BRSignXexp | 1110 | Branch if Op2’s exponent sign status bit is set
BRLoop8NZ | 1111 | Branch if LoopCnt>0
BRSignYexp | 0110 | Branch if Op1’s exponent sign status bit is set
BrNegExpTerm | 0101 | Branch if current negative exponent calculated
0 | 0000 | Immedate data 0
1 | 0001 | Immedate data 1
2 | 0010 | Immedate data 2
3 | 0011 | Immedate data 3
4 | 0100 | Immedate data 4
5 | 0101 | Immedate data 5
6 | 0110 | Immedate data 6
7 | 0111 | Immedate data 7
8 | 1000 | Immedate data 8
9 | 1001 | Immedate data 9
XDigCnt | 0001 | Select the XDigit counter
XDPCnt | 0010 | Select the XDP counter
XYDexpCnt | 0011 | Select the Dexp counter
XYSexpCnt | 0100 | Select the Sexp counter
X9Cnt | 0101 | Select the X9 counter
QLCnt | 0110 | Select the QL counter
FixDP | 0000 | Select the DP status bit
SignXexp | 0001 | Select the Op2 exponent sign status bit
NegExpTerm | 0010 | Select the negative exponent accumulation terminated status bit
SignX | 0011 | Select the Op2 sign status bit
SignY | 0100 | Select the Op1 sign status bit
SignYexp | 0101 | Select the Op1 exponent sign status bit
AssertError | 0110 | Select the Error status bit
SelCtl1 (I5br:I7)
SelCtl2 (I16:I18)
SelCtl3 (I19:I21)
RegCmd (I8:I13)
Branches (D3:D0)
Immediate Data Labels (D3:D0)
MicroInstruction Fields
SubAddB | 0 | Add Digit 0 of Y register with Digit 0 of X register
 | 1 | Subtract Digit 0 of X register from Digit 0 of Y register
CarryEn | 0 | Disable Carry In to Adder/Subtractor for one instruction
 | 1 | Enable Carry In to Adder/Subtractor for one instruction
KeyAck | 0 | NA
 | 1 | Write state of keyboard into keyboard register, reset sequencer loop counter
HWIntEn | 0 | NA
 | 1 | Enable branch to interrupt service routine if HWInt is active for one instruction
Add/Sub (I14:I15)
SEQ/DSKY (I22:I23)

## Slide 27
DSKY LOOP
Int Pending?
Light Dig0;
ROR Xreg
Light DigE;
Assert Kybrd Row0
Register Kybrd State
Key Detected?
Assert Kybrd Row1
Register Kybrd State
Key Detected?
Assert Kybrd Row2
Register Kybrd State
Key Detected?
Assert Kybrd Row3
Register Kybrd State
Key Detected?
Key Released?
Enable Display
Disable Display
Light Dig1;
ROR Xreg
Light Dig7;
ROR Xreg
Light Dig2;
ROR Xreg
Light Dig3;
ROR Xreg
Light Dig4;
ROR Xreg
Light Dig5;
ROR Xreg
Light Dig6;
ROR Xreg
Light Dig8;
ROR Xreg
Clr Regs
Pwr On Reset
DSKY Loop Top
No
No
No
No
No
No
Yes
yes
yes
yes
yes
yes
Inetrrupt Service
Routine

## Slide 28
SHL Xreg <- ImmDat
XDigCnt++
DPFixed?
SexpCnt ++
In Op1Ph?
DexpCnt - -
DexpCnt ++
XDpCnt ++
Set NegExpTerm
DSKY
1-9 Service Routine
yes
no
yes
no
Set DPFixed
DP First Key?
Set SignXexp
SHL Xreg <- 0
XDgiCnt ++
SexpCnt - -
In OpPh1?
DexpCnt - -
DexpCnt ++
DSKY
Dp Service Routine
yes
no
yes
no
SHl Xreg <- 0
SignXexp?
XDigEmpty ?
DSKY
XDigCnt ++
DpFixed?
XDpCnt ++
SecpCnt ++
In Op1Ph?
DexpCnt ++
DexpCnt - -
XDigCnt ++
XDpCnt ++
NegExpTerm?
SexpCnt - -
In Op1Ph?
DexpCnt - -
DexpCnt ++
*QL ++
yes
no
yes
no
yes
no
yes
no
yes
no
yes
no
Building operand with pos exp
Building operand with neg exp
0 as first key ignored
Integer part
Fractional part
0 accrues to neg exp
*Copy of DexpCnt used by Div
Zero Service Routine

## Slide 29
DPFirst?
Enter Op1 Service Routine
Set SignYexp
XDigEmpty
XDigCnt ++
Set FixDp
DPFixed?
Set FixDp
DexpCnt - -
SexpCnt - -
yes
no
yes
no
yes
no
Left Justify Xreg
Copy Xreg to Yreg
Copy SignX to SignY
Remove leading 0’s from Xreg
Exch Xreg <> Yreg
Set EOp1Ph
Clr X9
DSKY
InOp2?
CLR
no
DPFirst?
no
Decr XDig
DecrXDp
DPOvrfl?
no
DigEmpty?
JMP DSKY
yes
Dicard digits right of Dp
Decr Sexp
yes
Count digs of integer part
Decr XDig
DigEmpty?
no
yes
Decr Sexp
yes
SHSexpDexp
Ignore nonzero digits
Count digs of consecutive 0s
DpFree?
yes
no
LoadX9, X8
ShlX
X9==0?
no
LoadX9, X8
ShlX
Decr Xdig
X9==0?
Incr Sexp
yes
Incr Sexp
no
DigEmpty?
no
yes
yes
yes
no
CE Service Routine
DSKY

## Slide 30
Xreg : Array[8:1] of BCD digits
X9 : BCD digit
Yreg : Array[8:1] of BCD digits
Qreg : Array[8:1] of BCD digits
QL : BCD digit
Xdp : Integer[2:0]
DpFixed : Boolean
Sexp : Integer[3:0]
Dexp : Integer[3:0]
NegExpDPFixed : Boolean
Basic Register Model
Qreg = Yreg
Yreg = Xreg
Xreg = 0
Xreg = Xreg + Yreg
QL - -
QL == 0?
No
Xreg.SHR<-X9
Qreg.SHR<-0
Yes
INVXDP
OPCHAIN
X9 ++
CarryO
!CarryO
QL = Q0
Mult
Finished 8th pass
Pass 1-8
Align decimal points
Opr Subtr?
Invert SignX
SignX == SignY?
X = X+ Y
SignX == 1 And
SignY == 0?
Exch XY
X = X – Y
OPCHAIN
Add or Sub
Yes
No
SHRX<(“1”)
CarryO
!CarryO
Yes
No
Yes
No
isNeg
Exch XY
leaves Y=0
X = X – Y
!isNeg
Inner loop
AppendDivdn
Q0=Ql; QL=0
X=X-Y
isNeg
X=X+Y
QL ++
Finished 8th pass
AppendDindn
Q0=Ql; QL=0
INVXDP
OPCHAIN
InitDivdn
X=X-Y
AppendDvdn
XDPCnt - -
X=X+Y
isNeg
X=X+Y
tstdvdnd
restorex
Qreg = Yreg
Yreg = Xreg
Xreg = 0
Div
Pass 1-8
Outer loop
!isNeg
!isNeg

## Slide 31
Mult
Pos Exp: XDp placement is initialized by Sexp. Incremented once (XDp shifted right one digit) if the final Mult loop leaves a non-zero accumulation of CarryOs in X9.
Neg Exp: XDp placed in left most position. Sexp number of leading zeros right shifted into MSD of product, losing right most digits for each shift.
Div:
Pos Exp: XDp placement is initialized by Dexp. Decremented once (XDp shifted left one digit) if the minimum number of dividend digits needed to subtract the divisor with a positive result is one more than the divisor digits.
NegExp: XDp placed in left most position. Dexp number of leading zeros right shifted into MSD, losing rightmost digits for each shift.
Add/Sub:
If Dexp <= 0, then XDp = XDp(Op2) else XDp = XDp(Op2) + Dexp.
Exponent Computation
(XDp Placement)
FixDp
Sexp + +
Dexp + +
1:9
0
Dp
0:9
FixDp
Sexp - -
Dexp - -
Dp
Key
1st Key
Key
0:9
Key
NegExpFixed
Sexp - -
Dexp - -
1:9
Sexp - -
Dexp - -
0
Ent
Ent
FixDp
Sexp + +
Dexp - -
1:9
Dp
0:9
FixDp
Sexp - -
Dexp + +
Dp
Key
1st Key
Key
0:9
Key
NegExpFixed
Sexp - -
Dexp - -
1:9
Sexp - -
Dexp - -
0
Opr
Opr
XDp + +
XDp + +
Done
Op1Ph
Op2Ph
0

## Slide 32
ClrYPh2
Is X8==0?
Yes=NegExp
No=PosExp
Y=Q=QL=SignY=SignYExp=0; State=Idle
Incr XDp until overflow while incr Dexp
compensate for overshoot
CopyXY
goto EoPh1
Decr Sexp
ShlX
X8==0?
no
ExchXY
SHSexpDexp
Set SignYexp
Clr X9
Compute negative exponent in Sexp
X will be left justified here Y is copy of original
yes
NxtPh
no
no
Incr XDp
Incr Dexp
Decr Xdp
Decr Dexp
Incr Sexp
DpOvrfl?
DecEven?
Decr Sexp
SHSexpDexp
Restore XDp while computing exponent in Sexp
Operation Chaining
CopyXY
For 1..8
Loop Done?
no
ClrYPh2
Clr SignX
yes
Clr QL
SignX?
Set SignY
Result was 0
no
yes
(Post processing the result of an operation to support chaining)
Invert XDP
ClrYPh2
Decr Dexp
DintOvrfl?
Incr Dexp
Decr Dexp
Decr XDp
DpOvrfl
Incr Dexp
Copy Dexp to XDp
Compute Dexp=7-Dexp
Dexp=8
Dexp=7
Dexp=7-Dexp+1
Dexp=7-Dexp

## Slide 33
 |  |  |  | Xexp(+), Yexp(+) |  |  |  |  |  |  |  |  | Xexp(-),Yexp(+) |  |  |  | 
OP2(X) |  | 10000000 | 1000000 | 100000 | 10000 | 1000 | 100 | 10 | 1 |  | 0.1 | 0.01 | 0.001 | 0.0001 | 0.00001 | 0.000001 | 0.0000001
OP1 (Y) | exp | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | -1 | -2 | -3 | -4 | -5 | -6 | -7
10000000 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  | 8 | 9 | 10 | 11 | 12 | 13 | 14
1000000 | 6 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  | 7 | 8 | 9 | 10 | 11 | 12 | 13
100000 | 5 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 |  | 6 | 7 | 8 | 9 | 10 | 11 | 12
10000 | 4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 |  | 5 | 6 | 7 | 8 | 9 | 10 | 11
1000 | 3 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 |  | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 2 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 |  | 3 | 4 | 5 | 6 | 7 | 8 | 9
10 | 1 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 |  | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 0 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7
0.1 | -1 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
0.01 | -2 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 |  | -1 | 0 | 1 | 2 | 3 | 4 | 5
0.001 | -3 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 |  | -2 | -1 | 0 | 1 | 2 | 3 | 4
0.0001 | -4 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 |  | -3 | -2 | -1 | 0 | 1 | 2 | 3
0.00001 | -5 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 |  | -4 | -3 | -2 | -1 | 0 | 1 | 2
0.000001 | -6 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 |  | -5 | -4 | -3 | -2 | -1 | 0 | 1
0.0000001 | -7 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 |  | -6 | -5 | -4 | -3 | -2 | -1 | 0
 |  |  |  | Xexp(+), Yexp(-) |  |  |  |  |  |  |  |  | Xexp(-), Yexp(-) |  |  |  | 
Add Underflow
Add Underflow
Addition Overflow and Underflow
(DintOvrfl=1)(SignYexp=0)(SignXexp=1) Use Yreg
(DintOvrfl=1)(SignYexp=1)(SignXexp=0) Use Xreg
Add Overflow
(DintOvrfl=1)(SignYexp=0)(SignXexp=0) OR
(DintOvrfl=1)(SignYexp=1)(SignXexp=1)
Overflow happens when Op1 and Op2 are both 8-digit integers and the sum results in a final carry out digit 8.
Because SignYexp is only available to Mult and Div (due to arch oversight) I can’t
Use these expressions to detect underflow.
Op2(X) is DPFirst AND DintOVrfl
0000 | 0 | 
0001 | 1 | -15
0010 | 2 | -14
0011 | 3 | -13
0100 | 4 | -12
0101 | 5 | -11
0110 | 6 | -10
0111 | 7 | -9
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
Op2(X) is NOT DintOvrfl AND NOT DPFirst
9+0.0000001=9.0000001
99999999+.1=99999999
99+0.0000001=99
Dintovrfl=1
DPFirst=1
Dexp Counter values for All Op1 and Op2 Combinations

## Slide 34
Mult Overflows |  |  | 
Anytime Sexp is positive number greater than 7 |  |  | 
Within the positive exp1, positive exp2 quadrant |  |  | 
 |  | 0.0000001 | 0.0000001 | 0.000001 | 0.000001 | 0.00001 | 0.00001 | 0.0001 | 0.0001 | 0.001 | 0.001 | 0.01 | 0.01 | 0.1 | 0.1 | 0 | 0 | 1 | 1 | 10 | 10 | 100 | 100 | 1000 | 1000 | 10000 | 10000 | 100000 | 100000 | 1000000 | 1000000 | 10000000 | 10000000
A div C… |  | -7 | -7 | -6 | -6 | -5 | -5 | -4 | -4 | -3 | -3 | -2 | -2 | -1 | -1 |  |  | 0 | 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7
 |  | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp | Dexp | Sexp
0.0000001 | -7 | 0 | -14 | -1 | -13 | -2 | -12 | -3 | -11 | -4 | -10 | -5 | -9 | -6 | -8 |  |  | -7 | -7 | -8 | -6 | -9 | -5 | -10 | -4 | -11 | -3 | -12 | -2 | -13 | -1 | -14 | 0
0.000001 | -6 | 1 | -13 | 0 | -12 | -1 | -11 | -2 | -10 | -3 | -9 | -4 | -8 | -5 | -7 |  |  | -6 | -6 | -7 | -5 | -8 | -4 | -9 | -3 | -10 | -2 | -11 | -1 | -12 | 0 | -13 | 1
0.00001 | -5 | 2 | -12 | 1 | -11 | 0 | -10 | -1 | -9 | -2 | -8 | -3 | -7 | -4 | -6 |  |  | -5 | -5 | -6 | -4 | -7 | -3 | -8 | -2 | -9 | -1 | -10 | 0 | -11 | 1 | -12 | 2
0.0001 | -4 | 3 | -11 | 2 | -10 | 1 | -9 | 0 | -8 | -1 | -7 | -2 | -6 | -3 | -5 |  |  | -4 | -4 | -5 | -3 | -6 | -2 | -7 | -1 | -8 | 0 | -9 | 1 | -10 | 2 | -11 | 3
0.001 | -3 | 4 | -10 | 3 | -9 | 2 | -8 | 1 | -7 | 0 | -6 | -1 | -5 | -2 | -4 |  |  | -3 | -3 | -4 | -2 | -5 | -1 | -6 | 0 | -7 | 1 | -8 | 2 | -9 | 3 | -10 | 4
0.01 | -2 | 5 | -9 | 4 | -8 | 3 | -7 | 2 | -6 | 1 | -5 | 0 | -4 | -1 | -3 |  |  | -2 | -2 | -3 | -1 | -4 | 0 | -5 | 1 | -6 | 2 | -7 | 3 | -8 | 4 | -9 | 5
0.1 | -1 | 6 | -8 | 5 | -7 | 4 | -6 | 3 | -5 | 2 | -4 | 1 | -3 | 0 | -2 |  |  | -1 | -1 | -2 | 0 | -3 | 1 | -4 | 2 | -5 | 3 | -6 | 4 | -7 | 5 | -8 | 6
0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | 0 | 7 | -7 | 6 | -6 | 5 | -5 | 4 | -4 | 3 | -3 | 2 | -2 | 1 | -1 |  |  | 0 | 0 | -1 | 1 | -2 | 2 | -3 | 3 | -4 | 4 | -5 | 5 | -6 | 6 | -7 | 7
10 | 1 | 8 | -6 | 7 | -5 | 6 | -4 | 5 | -3 | 4 | -2 | 3 | -1 | 2 | 0 |  |  | 1 | 1 | 0 | 2 | -1 | 3 | -2 | 4 | -3 | 5 | -4 | 6 | -5 | 7 | -6 | 8
100 | 2 | 9 | -5 | 8 | -4 | 7 | -3 | 6 | -2 | 5 | -1 | 4 | 0 | 3 | 1 |  |  | 2 | 2 | 1 | 3 | 0 | 4 | -1 | 5 | -2 | 6 | -3 | 7 | -4 | 8 | -5 | 9
1000 | 3 | 10 | -4 | 9 | -3 | 8 | -2 | 7 | -1 | 6 | 0 | 5 | 1 | 4 | 2 |  |  | 3 | 3 | 2 | 4 | 1 | 5 | 0 | 6 | -1 | 7 | -2 | 8 | -3 | 9 | -4 | 10
10000 | 4 | 11 | -3 | 10 | -2 | 9 | -1 | 8 | 0 | 7 | 1 | 6 | 2 | 5 | 3 |  |  | 4 | 4 | 3 | 5 | 2 | 6 | 1 | 7 | 0 | 8 | -1 | 9 | -2 | 10 | -3 | 11
100000 | 5 | 12 | -2 | 11 | -1 | 10 | 0 | 9 | 1 | 8 | 2 | 7 | 3 | 6 | 4 |  |  | 5 | 5 | 4 | 6 | 3 | 7 | 2 | 8 | 1 | 9 | 0 | 10 | -1 | 11 | -2 | 12
1000000 | 6 | 13 | -1 | 12 | 0 | 11 | 1 | 10 | 2 | 9 | 3 | 8 | 4 | 7 | 5 |  |  | 6 | 6 | 5 | 7 | 4 | 8 | 3 | 9 | 2 | 10 | 1 | 11 | 0 | 12 | -1 | 13
10000000 | 7 | 14 | 0 | 13 | 1 | 12 | 2 | 11 | 3 | 10 | 4 | 9 | 5 | 8 | 6 |  |  | 7 | 7 | 6 | 8 | 5 | 9 | 4 | 10 | 3 | 11 | 2 | 12 | 1 | 13 | 0 | 14
OP1
OP2
OPMultDiv
DPOvrfl
DPFirst
OP1DPFrst
Error
OPMultDiv
DPOvrfl
DPFirst
OP1DPFrst
Error
(DPOvrfl=1)(SignYexp=SignXexp=0)
Mult Underflows
Div Underflows
(DPOvrfl=1)(SignYexp=SignXexp=1)
(DPOvrfl=1)(SignYexp=1)(SignXexp=0)
Division Overflows
Anytime Dexp is positive number greater than 7
Within the positive exp1, negative exp2 quadrant
(DPOvrfl=1)(SignYexp=0)(SignXexp=1)
Multiplication and Division Overflows and Underflows
Dexp and Sexp Counter Values From All Combinations of Op1 and Op2